## Slide 1: Evaluation of Coverage-Driven Random Verification
ECE 7502 – Project Presentation
Qing Qin
04/23/2015

## Slide 2
Requirements
Specification
Architecture
Logic / Circuits
Physical Design
Fabrication
Manufacturing Test
Packaging Test
PCB Test
System Test
PCB Architecture
PCB Circuits
PCB Physical Design
PCB Fabrication
Design and Test Development
Customer
Validate
Verify
Verify
Test
Test

## Slide 3: Problems
How to create a hierarchical testbench that can be shared by different tests?
How to model the DUT to predict the output results for random verification?
What coverage measurements can be used to monitor the verification process? How good are they?
How is functional verification related to manufacturing testing?
Notes: Directed testing
  Terribly long time to create stimuli vectors and write testbench for each test case
  Lack of metric to monitor the progres
Random Verification
Constrained-random stimulus generation
Functional coverage to measure progress
Common testbench for all test cases

## Slide 4: Hypothesis/Expected Outcome
Layered testbench with modeling capability
Define different coverage metrics and demo how to gather the measurement
Fault modeling in the context of verification
Approach
Floating-point adder as demo
Literature review

## Slide 5: Results: Layered Testbench
DUT
Driver
Input Monitor
Scoreboard
Output Monitor
Generator
Scenario
Command
Signal
Functional
Adapted from [1] Spear & Tumbush

## Slide 6: Results: Functional Coverage
Directed Verification
Random Verification
  Covergroup and Coverpoint

## Slide 7
Coverage | Count | Name
0.83 (75/90) | 12/16 | fpu_coverage.sign_mag
 | 4(1) | <a_neg,b_neg,a_small,a_small>
 | 6(1) | <a_neg,b_neg,a_small,a_big>
 | 0(1) | <a_neg,b_neg,a_big,a_small>
 | 0(1) | <a_neg,b_neg,a_big,a_big>
 | 1(1) | <a_neg,b_pos,a_small,a_small>
 | 1(1) | <a_neg,b_pos,a_small,a_big>
 | 1(1) | <a_neg,b_pos,a_big,a_small>
 | 1(1) | <a_neg,b_pos,a_big,a_big>
 | 1(1) | <a_pos,b_neg,a_small,a_small>
 | 1(1) | <a_pos,b_neg,a_small,a_big>
 | 1(1) | <a_pos,b_neg,a_big,a_small>
 | 3(1) | <a_pos,b_neg,a_big,a_big>
 | 3(1) | <a_pos,b_pos,a_small,a_small>
 | 3(1) | <a_pos,b_pos,a_small,a_big>
 | 3(1) | <a_pos,b_pos,a_big,a_small>

## Slide 8: Results: Code Coverage
Block Coverage
  A block is a statement or sequence of statements in Verilog/VHDL that executes with no branches or delays.
  Example: statements between begin and end keywords
Expression Coverage
  Measures how thoroughly a testbench exercises expressions in assignments and procedural control constructs (if/case conditions)
  Example: if (en == 1’b1) q <= d
Toggle Coverage
  Measures activity of various signals in a design and provides information on untoggled signals or signals that remain constant during simulation run
Notes: Code coverage: This will give information about how many lines are exected, how many times expressions, branches executed. This coverage is collected by the simulation tools. Users use this coverage to reach those corner cases which are not hit by the random testcases. Users have to write the directed testcases to reach the missing code covearage areas.
Functional coverage: This coverage will be defined by the user. User will define the coverage points for the functions to be covered in DUT. This is completly under user control.
Both of them have equal importance in the verification. 100% functional coverage does not mean that the DUT is completly exercised and vice-versa. Verification engineers will consider both coverages to measure the verifcation progress.
Let's say, the spec talks about 3 features, A, B, and C.
And let's say that the RTL designed coded only feature A and B.
If the test exercises only feature A and B, then you can 100% code coverage.
Thus, even if you have 100% code coverage, you have a big hole (feature C) in the design.
So, the verif engr, has to write funcitonal coverage code for A, B and C.
And 100% functional coverage means, there are tests for all the features, which the verif engr. has thought of.

## Slide 11: Results: RTL Fault Coverage
Difference between RTL Fault Coverage and Gate-Level Fault Coverage
  Input to fault simulator: HDL or netlist
  Expect correlation between the two fault coverage measurements
Motivation
  Improve testability of design and effectiveness of test patterns at an earlier stage
Fault Model: Single Stuck-at
  [2]: Single stuck-at fault for each bit of all variables in the RTL design
  [3]: Single stuck-at fault for more components in HDL

## Slide 12: Results: RTL Fault Coverage
Pessimistic or Optimistic Estimation
[2] Mao & Gulati

## Slide 13: Results: RTL Fault Coverage
[2] Mao & Gulati

## Slide 14: Results: RTL Fault Coverage
Chart: RTL Fault Coverage (%)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
系列 1 | 44.1176 | 67.3428 | 73.1237 | 75.2535 | 76.3692 | 82.1501 | 82.3529 | 82.3529 | 82.4544 | 84.5842

## Slide 15: Conclusions
Object-oriented layered testbench has some reusable verification classes。
Functional coverage is always defined by the verifier.
Neither 100% functional coverage nor code coverage guarantee a fully examined DUT.
Fault coverage can be predicted on an earlier stage at RTL design before synthesis.
Discussion and feedback is important!
Notes: How to create a hierarchical testbench that can be shared by different tests?
How to model the DUT to predict the output results for random verification?
What coverage measurements can be used to monitor the verification process? How good are they?
How is functional verification related to manufacturing testing?

## Slide 16: References
[1] C. Spear and G. Tumbush, SystemVerilog for Verification. New York, NY: Springer 2012
[2] Mao, W.; Gulati, R.K., "Improving gate level fault coverage by RTL fault grading," Test Conference, 1996. Proceedings., International , vol., no., pp.150,159, 20-25 Oct 1996
[3] Karunaratne, M.; Sagahayroon, A.; Prodhuturi, S., "RTL fault modeling," Circuits and Systems, 2005. 48th Midwest Symposium on , vol., no., pp.1717,1720 Vol. 2, 7-10 Aug. 2005